## Slide 1
IPyyy
myApps
WebRTC
IPxxx
Master PBX
App Platform
DNS Names |  | 
*.company.com Wildcard Certificate |  | 
Name | DNS Intern | DNS Extern
pbx.company.com | IPxxx IP | Public IP
apps.company.com | App Platform IP | Public IP
turn.company.com | IPyyy IP | Public IP
Reverse Proxy
TURN
Server
myApps
WebRTC
PC LAN
myApps
WebRTC
VoIP LAN
Management LAN
DMZ
1300
636
(80) 443
1300
1720
636
(80) 443
The reverse proxy needs port 1720 in addition to 1300 to the PBX for name registrations (e.g. free seating). Port 80 is not absolutely necessary, since http is already intercepted in the reverse proxy.
1300
636
80
443 > 8443
3478 TCP&UDP
TURN:
3478 TCP&UDP
To ensure that the TURN server is not used internally, as many networks as possible should reach each other for RTP. RTP: 16384 - 32767 & 50000 -50299 UDP
Public IP
DNS-Server Intern
myApps
WebRTC
DNS-Server Extern
Example PBX with Reverse Proxy & TURN
SIP SBC
IP address
Own IP-Adr.
IP address
WWW
RTP:
16384 - 32767
50000 - 50299
RTP
Switch off
SIP ALG!

## Slide 3
WebRTC
WebRTC
IP0011
Master PBX
Standby PBX
App Platform
DECT
DNS Names |  | 
*.ucc.company.com Wildcard Certificate |  | 
Name | DNS Intern | DNS Extern
pbx.ucc.company.com | Master PBX | Public IP
apps.ucc.company.com | App Platform | Public IP
turn.ucc.company.com | Turn Server | Turn Server
Reverse Proxy
TURN
Server
8.9.10.11
WWW
Firewall > Reverse Proxy:
80 TCP
443 TCP > 8443 TCP
1300 TCP
636 TCP
3478 TCP+UDP
IP411
IPVA
WebRTC
Slave PBX
DECT
SIP SBC
Network Design Template
Switch off
SIP ALG!

## Slide 4
IPxxx
Master PBX
Voice VLAN
999.999.999.999/32
VLAN X 999.999.999.999/32
WWW
Apps
WebRTC
Firewall Activations
Internet > Reverse Proxy :
80 TCP (nur Redirect)
443 TCP > 8443 TCP
1300 TCP
636 TCP
All Networks > TURN:
3478 TCP+UDP
Reverse Proxy > Voice VLAN
443 TCP
1300 TCP
1720 TCP
636 TCP
Apps
WebRTC
PC VLAN
Apps
WebRTC
80 (redirect only)
8443
1300
636
Public IP
Forwarding Public IP Addresses |  | 
From | To | Remark
Public IP 1 | x.x.x.x | Reverse Proxy
Public IP 2 | x.x.x.x | TURN Server 1
Public IP 3 | x.x.x.x | TURN Server 2
DNS Names |  | 
*.ucc.company.com Wildcard Certificate If "ucc.company.com" is also to be resolved, a multi-domain certificate is required! |  | 
Name | DNS Intern | DNS Extern
pbx.ucc.company.com | Master PBX | Reverse Proxy
apps.ucc.company.com | AP | Reverse Proxy
turn.ucc.company.com | TURN 1 TURN 2 | TURN 1 TURN 2
client.ucc.company.com or ucc.company.com | Conference Website | Reverse Proxy
IP3011
DSP Channels for Conf.
999.999.999.999/32
999.999.999.999/32
Apps
WebRTC
DMZ
IPxxx
Reverse Proxy
999.999.999.999/32
IPxxx
TURN Server 1
999.999.999.999/32
IPxxx
TURN Server 2
999.999.999.999/32
3478 TCP+UDP
3478 TCP+UDP
AP
Apps
999.999.999.999/32
AP
Apps
999.999.999.999/32
stun.sipgate.net
Network Design Example
Switch off
SIP ALG!

## Slide 5
DC Area 2
DC Area 1
Firewall
Cluster
Firewall Inbound NAT
Reverse Proxy
80, 443>8443, 1300, 636, 5060, 5061
203.0.113.22 > 10.1.1.10
203.0.113.22 > 10.1.1.11
TURN 3478 TCP&UDP
RTP 16384-32767 UDP (3rd Party SIP)
203.0.113.22 > 10.1.1.10
203.0.113.23 > 10.1.1.11
203.0.113.24 > 10.1.1.12
203.0.113.25 > 10.1.1.13
Other Firewall Rules
Any TCP and UDP for *.innovaphone.com, SIP provider incl. RTP, mail server, customer applications, etc.
HTTPS from TURN Server to Admin Apps
Reverse Proxy 1
cloud-rp01
10.1.1.10
Reverse Proxy 2
cloud-rp02
10.1.1.11
Admin PBX
admin01-pbx.cloud.tk
10.10.1.20
Admin Apps
admin01-apps.cloud.tk
10.10.2.20
TURN 1
cloud-turn01
172.16.1.10
TURN 2
cloud-turn02
172.16.1.11
cutomer 1 PBX
cutomer1-pbx.cloud.tk
10.10.1.21
cutomer 1 Apps
cutomer1-apps.cloud.tk
10.10.2.21
cutomer 2 PBX
cutomer2-pbx.cloud.tk
10.10.1.22
cutomer 2 Apps
cutomer2-apps.cloud.tk
10.10.2.22
cutomer … PBX
cutomerN-pbx.cloud.tk
10.10.1…
cutomer … Apps
cutomerN-apps.cloud.tk
10.10.2….
TURN 3
cloud-turn03
172.16.1.12
TURN 4
cloud-turn04
172.16.1.13
Mailserver
Addressbook (LDAP)
OAuth2
…
myApps
DECT
DECT
myApps
SIP
Network Design Example Cloud 1
Switch off
SIP ALG!

## Slide 6
UCC DMZ x.x.x.x/16
Public DMZ x.x.x.x/24
Reverse Proxy
STUN Server
TURN
WWW
IPVA License
License PBX
xx.xx.xx.xx
IPVA PBX 1
Master PBX
Webdav
SBC
xx.xx.xx.xx
SIP
IPVA PBX 2
Master PBX
Webdav
SBC
xx.xx.xx.xx
Firewall Activations
Internet > Reverse Proxy / STUN:
80 TCP (Nur für Redirect!)
443 TCP > 8443 TCP
1300 TCP
5060 TCP
5061 TCP
636 TCP
3478 TCP+UDP
Internet > TURN:
3478 TCP+UDP
UCC DMZ > STUN/TURN:
3478 TCP+UDP via External!!!
Reverse Proxys > UCC DMZ
443 TCP
1300 TCP
1720 TCP
5060 TCP
5061 TCP
636 TCP
SBC > SIP Provider:
5060/61 TCP or UDP (depending on the provider)
Internet > Reverse Proxy für ASEKO:
443 TCP
Reverse Proxy for Portal > Portal DMZ:
443 TCP
Portal DMZ > UCC DMZ:
443 TCP
636 TCP
TURN
Mgmnt. DMZ x.x.x.x/zz
DB
User
Portal
Admin
Portal
Mngmnt
LDAP Server
Reverse Proxy für Portal
Apps
WebRTC
Apps
WebRTC
cutomer 1
Exchange
Mailserver for Fax
Addressbook (LDAP)
Presence status
Apps
WebRTC
Apps
WebRTC
cutomer 2
Exchange
Mailserver for Fax
Addressbuch (LDAP)
Presence status
Network Design Example Cloud 2
App Platform
Apps
xx.xx.xx.xx
Switch off
SIP ALG!